physical computing .2 – Day 2
NCTU Taiwan
playaround workshop
microplayground
2008
kiilo ||| dusjagr

---
overview

---
Overview – Day 2
Digital Input / Output – Arduino
  - control sound machine
  - control voltage using a transistor
  - control relais and 110 V stuff
  - control hacked toys
Analog Input – Arduino
  - pduino
  - check serial
Programming Arduino

---
physical computing .2
let's start !

---
playaround fileserver
username: play
password: around
http://playaround.ftpaccess.cc/

---
physical computing
It is all about connection
HowTo connect to breadboard
HowTo communicate with Computer
HowTo connect your creativity
HowTo not getting confused?

---
physical connecting – power from arduino
Bridge the big gap!

---
Simple NAND oscillator
Control from Arduino

---
LM386 – Audio Amplifier Chip
Gain
Volume Control

---
Make it a bit less loud

---
Use PureData as Oscilloscope
http://playaround.ftpaccess.cc/project/physical+computing+2/outline/1.day/ oscilloscope_2.pd

---
Control the Noise machine from Arduino

---
How to connect things – 2 different ways
Pd_firmware.pde
Power &
cables
usb
in/out
Pduino-0.3.1/arduino-help.pd
Blink.pde
Change and
upload new
code
Power &
cables
usb power
in/out
battery power

---
Analog In
/*
* AnalogInput
*
* 1-bit music
* attach a speaker to pin 7 and GND
*
* dusjagr 2008
*/
int potPin = 0; // select the input pin for the potentiometer
int speakerPin = 7; // select the pin for the speaker
int val = 0; // variable to store the value coming from the sensor
void setup() {
pinMode(speakerPin, OUTPUT); // declare the speakerPin as an OUTPUT
}
void loop() {
val = analogRead(potPin); // read the value from the sensor
digitalWrite(speakerPin, HIGH); // turn the speakerPin on
delay(val); // stop the program for some time
digitalWrite(speakerPin, LOW); // turn the speakerPin off
delay(val); // stop the program for some time
}
GND
VCC