physical computing .2 – Day 3
NCTU Taiwan
playaround workshop
microplayground
2008
kiilo ||| dusjagr

---
overview

---
Overview – Day 3
Analog Inputs - Arduino
  - read sensors
Hack Toys
  - open it
  - hack the clock
Control Toys with Arduino
  - control motors
  - control recording unit
  - send simple messages to computer and from computer
Open Experiments and Help with Projects

---
How to connect things – 2 different ways
Pd_firmware.pde
Power &
cables
usb
in/out
Pduino-0.3.1/arduino-help.pd
Blink.pde
Change and
upload new
code
Power &
cables
usb power
in/out
battery power

---
physical computing .2
let's start !

---
Analog In – 1-Bit Music
http://playaround.ftpaccess.cc/project/physical+computing+2/outline/3.day _1bitmusic.pde
/*
* AnalogInput
*
* 1-bit music
* attach a speaker to pin 7 and GND
*
* dusjagr 2008
*/
int ldrPin = 1; // select the input pin for the potentiometer
int speakerPin = 7; // select the pin for the speaker
int val = 0; // variable to store the value coming from the sensor
void setup() {
pinMode(speakerPin, OUTPUT); // declare the speakerPin as an OUTPUT
Serial.begin(9800);
}
void loop() {
val = analogRead(ldrPin); // read the value from the sensor and shift 4 bits down 0-63
Serial.println (val); // send serial value to computer
digitalWrite(speakerPin, HIGH); // turn the speakerPin on
delayMicroseconds(val); // stop the program for some time
digitalWrite(speakerPin, LOW); // turn the speakerPin off
delayMicroseconds(val); // stop the program for some time
}

---
1-Bit Music
Tristan Perich
www.1bitmusic.com
Fredrik Oloffson
arduino workshop @ clubtransmediale
www.fredrikolofsson.com
or for some advanced chiptunes on microcontrollers
www.linusakesson.net

---
Other Sensors

---
What to do with sensor data?
Send data to pd
Use sensor data
to control toy
< or >
read sensor value

---
physical computing .2
let's hack some Toys

---
Control Motors

---
Control Recording Unit
http://playaround.ftpaccess.cc/project/physical+computing+2/outline/3.day recorder.pde

---
Digital In
GND
VCC
/*
* Button
* by DojoDave <http://www.0j0.org>
*
* Turns on and off a light emitting diode(LED) connected to digital
* pin 13, when pressing a pushbutton attached to pin 7.
*
* http://www.arduino.cc/en/Tutorial/Button
*/
int ledPin = 13; // choose the pin for the LED
int inputPin = 2; // choose the input pin (for a pushbutton)
int val = 0; // variable for reading the pin status
void setup() {
pinMode(ledPin, OUTPUT); // declare LED as output
pinMode(inputPin, INPUT); // declare pushbutton as input
}
void loop(){
val = digitalRead(inputPin); // read input value
if (val == HIGH) { // check if the input is HIGH
digitalWrite(ledPin, LOW); // turn LED OFF
} else {
digitalWrite(ledPin, HIGH); // turn LED ON
}
}

---
playaround fileserver
username: play
password: around
http://playaround.ftpaccess.cc/